## Slide 1
SESSION 1
Robotics Workshop
From Electronics to
Sumo Robot
Microcontrollers
Electronics
Sensors & Motors
Sumo Robot Competition

## Slide 2
SESSION 1
What is a Microcontroller?
Arduino UNO
Hands-On Robotics Workshop
01
An integrated circuit that combines a microprocessor, memory, and peripheral interfaces on a single chip is known as a microcontroller.
ATmega32P

## Slide 3
SESSION 1
Arduino UNO
Hands-On Robotics Workshop
02
Digital Pins
From 0 to 13 Special Func.
0,1 RX,TX
3,5,6,9,10,11 PWM
13 Built-in LED
Power Pins
3.3V & 5V
GND
Vin
Analog Pins
From A0 to A5

## Slide 4
SESSION 1
ESP32
Hands-On Robotics Workshop
03
GPIO Pins (Digital I/O):
GPIO 2, 4, 5, 18, 19, 21, 22, 23
Analog Pins (ADC):
GPIO 32 → 39
*Note: these pins are input only
Boot/Strapping Pins (Be Careful):
These affect startup behavior:
GPIO 0
GPIO 2
GPIO 12
GPIO 15
Pins to avoid (Be careful):
GPIO 6–11 → used internally for flash memory
GPIO 34–39 → input only (no output)

## Slide 5
SESSION 1
Signal Types
Hands-On Robotics Workshop
04
Digital signal
Analog signal
ADC
ADC is an electronic circuit that converts a signal from analog form (continuous) into digital form (discrete), so that the processor can read it as an ordinary number.

## Slide 6
SESSION 1
can we talk to a microcontroller?
Hands-On Robotics Workshop
05
Arduino IDE
The Arduino IDE (Integrated Development Environment) is the software you use to write, compile, and upload code to Arduino boards/Other Boards.

## Slide 7
SESSION 1
Coding intro
Hands-On Robotics Workshop
06
Call back functions
API’s
Void setup()
Void loop()
pinMode()
digitalRead() digitalWrite() analogRead()
Parameters & Arguments
Parameter = the placeholder variable in the function's definition. It's the name used inside the function to refer to whatever gets passed in.
Argument = the actual value you pass in when you call the function.
Variable definition
Define Variable types, names.
Define used Pins.
Let’s take look on these items in the IDE

## Slide 8
SESSION 1
Breadboard
Hands-On Robotics Workshop
07
Each vertical line with 5 Dots is connected
Each horizontal line is connected

## Slide 9
SESSION 1
Hands-On Robotics Workshop
08
Resistor
Push button
LED

## Slide 10
SESSION 1
Pull up vs. Pull down
Hands-On Robotics Workshop
09
Floating Pin
A pin that is not connected to any defined voltage (neither VCC nor GND), so it picks up random electrical noise from the environment and gives unpredictable HIGH/LOW readings.
Pull Up
Pull Down
Resistor is connected to Vcc.
Pressed = OFF
Unpressed = ON
Resistor is connected to GND.
Pressed = ON
Unpressed = OFF

## Slide 11
SESSION 1
Exercise_1: LED Blink
Hands-On Robotics Workshop
10
1- Open simulation software (Proteus ) do the wiring
2- Open IDE and write the code
3- Burn the code on the microcontroller

## Slide 12
SESSION 1
LAB_1
Hands-On Robotics Workshop
11
Use 3 LEDs, blink them to make the pattern you want
Try on simulation first, then hardware

## Slide 13
SESSION 1
Conditional if
Hands-On Robotics Workshop
12
if (condition1) {
// runs if condition1 is true
}
else if (condition2) {
// runs if condition1 is false AND condition2 is true
}
else {
// runs if none of the above are true
}

## Slide 14
SESSION 1
Exercise_2: LED Blink+Button
Hands-On Robotics Workshop
13
1- Open simulation software (Proteus ) do the wiring
2- Open IDE and write the code
3- Burn the code on the microcontroller

## Slide 15
SESSION 1
LAB_2
Hands-On Robotics Workshop
14
Use 3 LEDs, blink them using the switches
Try on simulation first, then hardware

## Slide 16
Thank You